Placement Exercise

 a) -seed <int>: Sets the initial random seed used by the placer. Default: 1.
Using the -seed option with seed values 1, 5, 7 and 15, following results were obtained with vpr:
Benchmark circuit / (No. Of netlist primities)	Seed value	bb_cost		Percentage Reduction in bb_cost	Runtime(mm:ss)	Placement cost		timing_cost		delay_cost
		Initial	Final			Initial	Final	Initial	Final	Initial	Final
Apex2 / (1116)	1	894.188	280.12	68.67%	0:42.59	0.996	0.879	1.27e-4	6.23e-6	1.41e-4	7.27e-5
	5	903.734	280.641	68.94%	0:42.98	0.994	0.836	1.27e-4	3.61e-6	1.40e-4	7.23e-5
	7	894.452	279.275	68.78%	0:43.17	0.980	0.851	1.26e-4	6.04e-6	1.39e-4	7.16e-5
	15	904.57	279.799	69.07%	0:43.25	1.00682	0.893	1.27e-4	5.19e-6	1.40e-4	7.28e-5

Frisc / (3291)	1	2271.44	587.227	74.15%	1:51.29	0.999	0.939	1.21e-4	3.87e-6	3.29e-4	1.39e-4
	5	2275.88	589.02	74.12%	1:54.66	1.00763	0.941	1.21e-4	6.37e-6	3.29e-4	1.36e-4
	7	2252.98	587.466	73.92%	1:53.71	0.991	0.941	1.18e-4	6.11e-6	3.22e-4	1.44e-4
	15	2249.87	593.212	73.63%	1:53.10	0.991	0.947	1.18e-4	7.12e-6	3.22e-4	1.36e-4

s38417 / (4888)	1	5835.43	687.198	88.22%	5:18.81	0.995	0.572	4.60e-4	6.77e-6	6.94e-4	1.85e-4
	5	5828.23	689.025	88.18%	4:49.80	1.00278	0.577	4.65e-4	7.98e-6	7.05e-4	1.83e-4
	7	5827.58	694.011	88.09%	4:55.78	0.986	0.604	4.51e-4	3.79e-6	6.83e-4	1.79e-4
	15	5790.68	686.778	88.14%	5:07.13	0.987	0.567	4.53e-4	3.68e-6	6.84e-4	1.87e-4

        Table 1
Inferences:
* Since, seed value determines the initial random placement, the initial bb_cost varies with the seed value for each benchmark circuit.
* “Percentage reduction in bb_cost” (highlighted in green) and “final bb_cost” (highlighted in turqoise) seem to be independant of the seed value for the 3 benchmark circuits.
* Final bb_cost achived is very close (Low standard deviation) for the four seed values for each benchmark circuit:

Benchmark Circuit	Average final bb_cost	Standard deviation
apex2	279.96	0.57
frisc	589.23	2.77
s38417	689.25	3.32

* Percentage reduction achieved in bb_cost increases with design size i.e number of netlist primitives
* Runtime for the vpr seems to be independant of the seed value but depends on the design size (as expected).

b) -inner_num <float>: The number of moves attempted at each temperature is inner_num times the total number of blocks 4/3 in the circuit. The number of blocks in a circuit is the number of pads plus the number of clbs. Changing inner_num is the best way to change the speed/quality tradeoff of the placer, as it leaves the highly-efficient automatic annealing schedule on and simply changes the number of moves per temperature. Default: 10. Note: specifying -inner_num 1 will speed up the placer by a factor of 10 while typically reducing placement quality only by 10% or less (depends on the architecture). Hence users more concerned with CPU time than quality may find this a more appropriate value of inner_num.

Using the -inner_num option with inner_num values 1, 10, and 20, following results were obtained with vpr:

        Table 2

Benchmark circuit / (No. Of netlist primities)	Inner num value	bb_cost		Percentage Reduction in bb_cost	Runtime(mm:ss)	Placement cost		timing_cost		delay_cost
		Initial	Final			Initial	Final	Initial	Final	Initial	Final
Apex2 / (1116)	1	894.188	290.454	67.51%	00:04.90	0.996	0.993	1.27e-4	7.05e-6	1.41e-4	6.88e-5
	10	894.188	280.12	68.67%	00:44.05	0.996	0.879	1.27e-4	6.23e-6	1.41e-4	7.27e-5
	20	894.188	275.449	69.19%	01:24.26	0.996	0.897	1.27e-4	3.28e-6	1.41e-4	7.26e-5

Frisc / (3291)	1	2271.44	681.733	69.99%	00:12.53	0.999	0.997	1.21e-4	4.63e-6	3.29e-4	1.55e-4
	10	2271.44	587.227	74.15%	01:54.53	0.999	0.939	1.21e-4	3.87e-6	3.29e-4	1.39e-4
	20	2271.44	586.742	74.17%	03:47.84	0.999	0.959	1.21e-4	6.14e-6	3.29e-4	1.38e-4

s38417 / (4888)	1	5835.43	726.34	87.55%	00:34.60	0.995	0.960	4.60e-4	1.29e-5	6.94e-4	1.70e-4
	10	5835.43	687.198	88.22%	04:54.88	0.995	0.572	4.60e-4	6.77e-6	6.94e-4	1.85e-4
	20	5835.43	671.954	88.48%	09:11.89	0.995	0.549	4.60e-4	5.31e-6	6.94e-4	1.86e-4

Inferences:

* Since, number of moves attempted at each temperature is a multiple of inner_num, hence, increasing inner_num value increases the runtime of the simulated annealing algorithm. As can be seen from table 2 above, runtime is maximum for inner_num value of 20 for each benchmark circuit. Similarly, the minimum runtime was seen with inner_num value of 1.
* Also, the quality of results i.e. the bb_cost achieved, improves with higher number for inner_num. This is because the number of moves attempted at each temperature increases with increase in inner_num value. For each benchmark circuit, the best placement was achieved (lowest bb_cost) for inner_num = 20
* As was the case with different seed values, the maximum runtime is seen for design with maximum number of blocks i.e. s38417

c)
-fast: Sets various placer and router parameters so that a circuit will be placed and routed more quickly, at the cost of some (~10 - 15%) degradation in quality. Note: -fast should probably not be used with the timing-driven router, as it can degrade the circuit speed by over 30%, without significantly speeding the router.

Benchmark circuit / (No. Of netlist primities)	Fast option	bb_cost		Percentage Reduction in bb_cost	Runtime(mm:ss)	Placement cost		timing_cost		delay_cost
		Initial	Final			Initial	Final	Initial	Final	Initial	Final
Apex2 (1116)	Yes	894.188	290.454	67.52%	0:04.75	0.996	0.993	1.27e-4	7.05e-6	1.41e-4	6.88e-5
	No	894.188	280.12	68.67%	0:42.18	0.996	0.879	1.27e-4	6.23e-6	1.41e-4	7.27e-5

Frisc (3291)	Yes	2271.44	681.733	69.98%	0.12.22	0.999	0.997	1.21e-4	4.63e-6	3.29e-4	1.55e-4
	No	2271.44	587.227	74.15%	1:51.60	0.999	0.939	1.21e-4	3.87e-6	3.29e-4	1.39e-4

s38417 (4888)	Yes	5835.43	726.34	87.55%	0:30.34	0.995	0.960	4.60e-4	1.29e-5	6.94e-4	1.70e-4
	No	5835.43	687.198	88.22%	4:35.98	0.995	0.572	4.60e-4	6.77e-6	6.94e-4	1.85e-4

        Table 3

Inferences:
* Runtime was reduced to 10-15% of the original runtime when the -fast option is used.
* Although, a slight degradation is seen in the bb_cost achieved.
* Initial placement remained unaffected due to the -fast option.

=> The runtime for the various runs was obtained through the “time” command. vpr tool was run as an argument to the time command.