Routing Exercise

Solution:
a)
* Channel routing instance can be represented as:

       column: 1 2 3 4 5 6 7 8 9 10
        2 3 3 6 7 1 6 5 4

        1 3 2 7 3 7 4 1 5

Figure 1: Channel Routing Instance.

* Decomposing each multi-pin net into 2-pin connections:

     column: 1 2 3 4 5 6 7 8 9 10
        2 3 3 6 7 1 6 5 4

2
1

3

4
5

6

7

        1 3 2 7 3 7 4 1 5
Figure 2: Multi-pin net decomposition
       density: 1 3 3 4 4 4 3 3 3 2

Hence, the local desities for columns 1-10 are: 1, 3, 3, 4, 4, 4, 3, 3, 3, 2
i.e ld(1) = 1, ld(2) = 3, ld(3) = 3, ld(4) = 4, ld(5) = 4
     ld(6) = 4, ld(7) = 3, ld(8) = 3, ld(9) = 3, ld(10) = 2

Therefore, the channel density, d = max{ ld(C) } over all C
        = 4

        i.e. d = 4

b)

7
3

1
5

Figure 3: Vertical constraint graph (VCG) for
        Channel Routing instance.

4
2
6

        Lower bound for number of tracks (without doglegs) = Longest path in VCG = 6

c)

5
4
1
2
6
3
7

Figure 4: Horizontal constraint graph (HCG) for
        Channel Routing instance.

Channel density (lower bound on number of tracks needed for routing) = Maximal clique in HCG
        = 4

d) Channel-length, λ = 10

        Top connection list, T = (2, 3, 3, 6, 0, 7, 1, 6, 5, 4)
        Bottom connection list, B = (0, 1, 3, 2, 7, 3, 7, 4, 1, 5)

        Left connection set, L = { 2 }
        Right connection set, R = {4, 5}

        H(1) = 9, H(2) = 4, H(3) = 6, H(4) = 10, H(5) = 10,
        H(6) = 8, H(7) = 7

        initial-channel-width = 4
        minimum-jog-length = w/4 = 1 ( w=4, i.e. best channel width obtainable)
        steady-net-constant = 10
        In the following diagrams, orange lines indicate jogs.
* Assign tracks to nets at left end: => Y(2) = {1}

Column 1:
    a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T1 = 2 to track 1 => Y(2) = {1} => No split nets => No need for step (b), (c)
     d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Add jog to to lower falling net 2 to an empty track ( track 4) which is as close as
        possible to its target edge. => Y(2) = {4}
     * No need for step (e) i.e. no need to widen channel
   f) Extend to Next Column

        2 3 3 6 7 1 6 5 4

Figure 5: Routing for
given routing instance
after column 1 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 2:

 a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T2 = 3 to track 1 and B2 = 1 to track 3.
        => Y(2) = {4}, Y(3) = {1}, Y(1) = {3} => No split nets => No need for steps (b) and (c)

      * No need for step (d) because net 2 is already closest to its target edge and net 3 and net 1 are
        steady nets.
      * No need for step (e) i.e. no need to widen channel
  f) Extend to next column

        2 3 3 6 7 1 6 5 4
Figure 6 : Routing for
given routing instance
after column 2 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

 Column 3:
        a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T3 = 3 to track 1 and B3 = 3 to track 2. => Y (2) = {4}, Y(3) = {1,2},
        Y(1) = {3} => | Y(3)| > 1
        i.e. net 3 is a split net or a collapsible net.
        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Added pattern of one “collapsing jog” to connect tracks 1 and 2, both holding net 3.
        This pattern free's up one track => Y(3) = {2}, Y(2) = {4}, Y(1) = {3}

        * No need for step (c) since, no split nets remain.
        * No need for step (d) since, because net 2 is already closest to its target edge and net 1 is a
        steady nets. Jog is already added in step b which brings falling net 3 closest to its target
        edge.
        * No need for step (e) because T3 and B3 were brought in to the track.
        f) Extend to next column

        2 3 3 6 7 1 6 5 4
Figure 7: Routing for
given routing instance
after column 3 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 4:
   a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T4 = 6 to track 1 and B4 = 2 to track 4 i.e. track already assigned to this net.
        => Y(2) = {}, Y(3) = {}, Y(1) = {3}, Y(6) = {1} => No split nets => No need for steps
        (b) and (c)

      * No need for step (d) because net 6 is already closest to its target edge and net 1 is a
        steady net.
       * No need for step (e) i.e. no need to widen channel because T4 and B4 were brought in to the
        channel
  f) Extend to next column

        2 3 3 6 7 1 6 5 4
Figure 8: Routing for
given routing instance
after column 4 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 5:

  a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect B5 = 7 to track 4 i.e. to the nearest possible track which is empty.
        => Y(2) = {}, Y(3) = {2}, Y(1) = {3}, Y(6) = {1}, Y(7) = {4}
        => No split nets => No need for steps (b) and (c)

      * No need for step (d) because net 6 is already closest to its target edge and net 1 and net 3 are
        steady net. Tracks 1, 2 and 3 are already occupied so net 7 is as close as possible to its target
        edge.
      * No need for step (e) i.e. no need to widen channel because T5 is a vacant terminal and B5 was
        brought in to the channel
  f) Extend to next column

        2 3 3 6 7 1 6 5 4

Figure 9: Routing for
given routing instance
after column 5 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 6:
   a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Since, T6 ≠ B6 and the vertical segments from the two terminals would conflict
        (overlap) then bring in B6 since it can be brought in with the least wire and we leave the
        other net to be brought in at step (e). This “finishes” net 3.
        => Y(2) = {}, Y(3) = {}, Y(1) = {3}, Y(6) = {1}, Y{7} = {4}
        => No split nets => No need for steps (b) and (c)
      * No need for step (d) because net 6 is already closest to its target edge and net 1 is a
        steady net. Tracks 1, 2 and 3 are already occupied so net 7 is as close as possible to its target
        edge.
  e) Widen Channel If Needed To Make Previously Infeasible Top Or Bottom Connection:
        Since, T6 = 7 could not be brought in to a track in step (a), we create a new track for this
        net and bring the net in to this track. The track is placed to be track 2 so that it is as near
        the center of the channel as possible between existing tracks. Modify the number of the
        tracks after this step.
        Also, the Y(n) values are updated as:
        =>Y(6) = 1, Y(7) = {2, 5}, Y(3) = {}, Y(1) = 3, Y(2) = {}

  f) Extend to next column
        2 3 3 6 7 1 6 5 4
Figure 10: Routing for
given routing instance
after column 6 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 7:

        a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T7 = 1 to track 3 and B7 = 7 to track 4 i.e. track already assigned to this net.
        => Y(2) = {}, Y(3) = {}, Y(1) = {3,4}, Y(6) = {1}, Y(7) = {2,5}

        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Added pattern of one “collapsing jog” to connect tracks 3 and 4, both holding net 1.
        This pattern free's up one track
        => Y(3) = {}, Y(2) = {}, Y(1) = {4}, Y(6) = {1}, Y(7) = {2,5}
        c) Add Jogs To Reduce The Range of Split Nets:
        Although, split nets exist(net 7), jogs cannot be added in this step because it would be
        incompatible with vertical wiring already placed in this column by step (b).
        d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Net 6 is already closest to its target edge. Jog has already been added for net 1 (now a falling
        net) to bring it closer to its target edge. Net 7 is a steady net now.

        * No need for step (e) i.e. no need to widen channel because T7 and B7 were brought in to the
        channel

  f) Extend to next column
        2 3 3 6 7 1 6 5 4

Figure 11: Routing for
given routing instance
after column 7 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 8:
        a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T8 = 6 to track 1 i.e. track already assigned to this net and B8 = 4 to track 3 i.e.
        to the nearest possible track which is empty. This finishes net 6.
        => Y(2) = {}, Y(3) = {}, Y(1) = {4}, Y(6) = {}, Y(7) = {2,5}, Y(4) = {3} => Net 7 is a
        split net

        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Although, split nets exist(net 7), “collapsing jogs” cannot be added in this step because
        the jog placed for net 7 between tracks 2 and 5 would overlap vertical wiring for net 4
        placed in step (a).
       c) Add Jogs To Reduce The Range of Split Nets:
        Although, split nets exist(net 7), jogs cannot be added in this step because it would be
        incompatible with vertical wiring already placed in this column by step (a).
        d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Net 4 is already closest to its target edge because tracks 1 and 2 are already occupied. Net 1
        (which is a falling net) is already closest to its target edge. Net 7 is a steady net.

        * No need for step (e) i.e. no need to widen channel because T8 and B8 were brought in to the
        channel

        f) Extend to next column

        2 3 3 6 7 1 6 5 4

Figure 12: Routing for
given routing instance
after column 8 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 9:
        a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect B9 = 1 to track 4 i.e. track already assigned to this net and T9 = 5 to track 1 i.e.
        to the nearest possible track which is empty. This finishes net 1.
        => Y(2) = {}, Y(3) = {}, Y(1) = {}, Y(6) = {}, Y(7) = {2,5}, Y(4) = {3}, Y(5) = {1}
        => Net 7 is a split net

        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Although, split nets exist(net 7), “collapsing jogs” cannot be added in this step because
        the jog placed for net 7 between tracks 2 and 5 would overlap vertical wiring for net 1
        placed in step (a).
       c) Add Jogs To Reduce The Range of Split Nets:
        Although, split nets exist(net 7), jogs cannot be added in this step because it would be
        incompatible with vertical wiring already placed in this column by step (a).
        d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Net 4 is already closest to its target edge because tracks 1 and 2 are already occupied. Net 7
        is a steady net. Net 5 is already closest ot its target edge because the remaining tracks are
        already occupied.

        * No need for step (e) i.e. no need to widen channel because T9 and B9 were brought in to the
        channel

        f) Extend to next column

        2 3 3 6 7 1 6 5 4

Figure 13: Routing for
given routing instance
after column 9 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 10:
        a) Make Feasible Top and Bottom Connections in Minimal Manner:
        Connect T10 = 4 to track 3 i.e. track already assigned to this net and B10 = 5 to track 4 i.e.
        to the nearest possible track which is empty. This finishes net 4.
        => Y(2) = {}, Y(3) = {}, Y(1) = {}, Y(6) = {}, Y(7) = {2,5}, Y(4) = {}, Y(5) = {1,4}
        => Net 7 and net 5 are split nets

        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Although, split nets exist(net 7 and net 5), “collapsing jogs” cannot be added in this step
        because the jog that would be placed for net 7 or net 5 would overlap vertical wiring for
        net 4 placed in step (a).
       c) Add Jogs To Reduce The Range of Split Nets:
        Although, split nets exist(net 7 and net 5), jogs cannot be added in this step because it
        would be incompatible with vertical wiring already placed in this column by step (a).
        d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Net 7 and net 5 are steady nets so need for step (d)
        * No need for step (e) i.e. no need to widen channel because T10 and B10 were brought in to
        the channel

        f) Extend to next column

        2 3 3 6 7 1 6 5 4

Figure 14: Routing for
given routing instance
after column 10 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 11:
        * No need for step (a) because there are no terminal pins in column 11.
        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Place collapsing jog randomly for net 7 because tracks 1 and 4 for net 5 & tracks 2 and 5
        for net 7 are symmetric, hence, both nets leave the outermost uncollapsed split net equally
        far from the channel edge. This completes net 7.
        => Y(2) = {}, Y(3) = {}, Y(1) = {}, Y(6) = {}, Y(7) = {}, Y(4) = {}, Y(5) = {1,4}
        => Net 5 is a split net.

       c) Add Jogs To Reduce The Range of Split Nets:
        Although, split net exists(net 5), jogs cannot be added in this step because it
        would be incompatible with vertical wiring already placed in this column by step (b).
        d) Add Jogs to Raise Rising Nets and Lower Falling Nets:
        Net 5 is a steady net so need for step (d)
     * No need for step (e) i.e. no need to widen channel because there are no terminals in column 11.
        f) Extend to next column

        2 3 3 6 7 1 6 5 4

Figure 15: Routing for
given routing instance
after column 11 has
been routed using rules
 as per greedy channel
 router algorithm.

        1 3 2 7 3 7 4 1 5

Column 12

      * No need for step (a) because there are no terminal pins in column 11.
        b) Free Up As Many Tracks As Possible By Collapsing Split Nets:
        Place collapsing jog for net 5. This completes net 5.
        => Y(2) = {}, Y(3) = {}, Y(1) = {}, Y(6) = {}, Y(7) = {}, Y(4) = {}, Y(5) = {}
     * No need for step (c) because there are no split nets.
     * No need for step (d) because there are no rising or falling nets.
     * No need for step (e) i.e. no need to widen channel because there are no terminals in column 12.
     * Since, there are no split nets that remain to be collapsed and column 12 ≥ 10, the greedy channel router ends.

        2 3 3 6 7 1 6 5 4

Figure 16: Routing for
given routing instance
after column 12 has
been routed using rules
 as per greedy channel
 router algorithm.

This is the final routing
Solution obtained.

        1 3 2 7 3 7 4 1 5